## Slide 1: Introduction to Networking
Lecture 1
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Basic networking concepts
IP and MAC addresses
Traffic types
OSI and TCP/IP models
Cisco Packet Tracer: Introduction

## Slide 3
Basic networking concepts

## Slide 4: What is a computer network?
Multiple computers linked together
Why? To communicate and share resources

## Slide 5: Why computer networking is important
Services, consumed by the users, depend on computer networks
Can be ungrateful and “dirty”
  when it works: “You are doing nothing!”
  when it doesn’t work: “It is down again!”

## Slide 6: How did it start?
ARPANET - The Advanced Research Projects Agency NETwork
Established in 1969
It is the first packet switching network which will use TCP/IP
It was designed for scientific purposes and to share computer resources
ARPANET’s purpose was more academic than military

## Slide 7: Common Types of Computer Networks
Local Area Network (LAN)
Wide Area Network (WAN)
Wireless Local Area Network (WLAN)
Storage Area Network (SAN)
Home Area Network (HAN)

## Slide 8: Local Area Network (LAN)
Connects network devices over a relatively short distance
Very useful for sharing resources such as data storage and printers

## Slide 9: Wide Area Network (WAN)
Connects multiple LANs together
Extends over a large geographical distance
The Internet is the largest WAN spanning the Earth

## Slide 10: Wireless Local Area Network (WLAN)
Links two or more devices using a wireless distribution method
Operates within limited area

## Slide 11: Storage Area Network (SAN)
Provides block-level network access to storage
The OS will see it as a locally attached storage
Common SAN protocols
  FC
  iSCSI
  AoE (ATA over Ethernet)

## Slide 12: Home Area Network (HAN)

## Slide 13: Common Types of Networking Devices
Hub (obsolete, not secure and very slow)
Switch
Router
Modem
Firewall
Bridge (like a Switch, fewer ports)
Repeater (like a Hub, it just amplifies the signal)

## Slide 14: Ethernet Hub
Used to connect multiple network hosts
Works at Layer 1 of the OSI model
Poor security and performance
Obsolete and now replaced by switches

## Slide 15: Ethernet Switch
Provides end user connectivity
More intelligent than a hub
Has a MAC address table
Provides Layer 2 functionality (and optionally L3)
VLANs can be configured

## Slide 16: Router
Sends packets from one network to another
Provides Layer 3 functionality
Uses IP addresses to transfer packets
“Traffic police” - directs the network traffic to different destinations

## Slide 17: Modem
Digital to analog (and vice versa) signal conversion: MOdulation/DEModulation

## Slide 18: Firewall
Monitors the network traffic and makes decisions what to allow and what to block
Protects a computer network from unauthorized access
It may be hardware device, a software, or a combination of the two

## Slide 19: Firewall (2)

## Slide 20: Bridge and repeater
Bridge
Similar to a Switch
Works at Layer 2
Repeater
Similar to a Hub
Works at Layer 1

## Slide 21: Types of Network Topologies
Physical vs logical topologies
(extended) star is the most common
Hybrid topologies

## Slide 22: Networks Protocols
Define a common format and set of rules for exchanging messages between network devices
Common protocols:
  HTTP
  FTP
  SMTP
  DNS
  DHCP
  RDP

## Slide 23: Hyper text transfer protocol (HTTP)
Set of rules to transfer files - text, images, sound, video and other multimedia on the World Wide Web
This is how our browsers talk to web servers

## Slide 24: File Transfer Protocol (FTP)
Transfer files from one computer to another
You can connect anonymously or with username and password

## Slide 25: Simple Mail Transfer Protocol (SMTP)
Can be used for:
  Server-to-server email transport
  Client-to-server email transport

## Slide 26: Domain Name System (DNS)
Translates domain names into IP addresses (and much more)
It is hierarchical and distributed database

## Slide 27: Dynamic Host Configuration Protocol (DHCP)
Allows a computer to get an IP address from a special server
Uses client-server architecture

## Slide 28: Remote Desktop Protocol (RDP)
Provides a graphical interface to connect to another computer over the network
Can also transfer other resources between the local and remote system, like audio, disk drives and clipboard

## Slide 29: Common Types of Media
“X”TP (“something” Twisted Pair). The “twist” idea introduced by Alexander Bell in 1881
Coaxial Cable
Fiber Optic
Wireless

## Slide 30: Let’s talk about cables…

## Slide 31: “X”TP (“something” Twisted Pair)
UTP – Unshielded Twisted Pair
S/UTP – Screened UTP
STP – Shielded Twisted Pair
S/STP - Screened STP

## Slide 32: EIA/TIA Standards
EIA = Electronic Industries Alliance TIA = Telecommunications Industry Association
T568B is most frequently used

## Slide 33: Straight-through Cable
Pin 1  Pin 1
Pin 2  Pin 2, etc.
Most commonly used to connect devices from different types:
  Host to switch
  Switch to router

## Slide 34: Straight-through Cable (2)
A “straight” cable can be either:
  T568B to T568B OR
  T568A to T568A

## Slide 35: Crossover Cable
Pin 1  Pin 3
Pin 2  Pin 6, etc.
Most commonly used to connect two hosts directly

## Slide 36: Crossover Cable (2)
It is T568B from one side and T568A from the other
Used to connect devices from the same type:
  Host to host
  Router to router
  Host to router (yes, no mistake)

## Slide 37: Auto MDI/MDIX
MDI: Medium Dependent Interface – standard wiring for end stations
MDIX: Medium Dependent Interface Crossover - standard wiring for hubs and switches
The good news! Auto MDI/MDIX automatically detects the required cable connection type and configures the connection appropriately

## Slide 38: Console Cable
Used to connect to the console of a networking device (switch, router)
Usually a USB to Serial adapter is also required

## Slide 39
IP and MAC addresses

## Slide 40: IP Addresses
Known as logical address
Can be assigned to network and end devices
Essential part in routing
Four bytes (octets), separated with “ . “ Example: 1.3.2.8

## Slide 41: IP Addresses (2)

## Slide 42: MAC Addresses
Known as physical address
Unique identifier assigned to network interfaces
48 bits or 6 bytes in a hexadecimal format (discussed later in the course)
Can you change it?

## Slide 43: What is a MAC Address Used for?
Host-to-host communication
Device Identification and tracking
“Static” IP Assignment (Matched MAC -> receive IP)
MAC Address Filtering
MAC Address Authentication (ISPs use it, for example)

## Slide 44: Example of MAC Address
Windows
Linux

## Slide 45: How to Modify a MAC Address in Windows

## Slide 46: How to Modify a MAC Address in Linux
The new MAC address

## Slide 47
Traffic Types

## Slide 48: Types of traffic

## Slide 49: Unicast

## Slide 50: Unicast (2)
Single destination identified by a unique address
Used in host-to-host or host-to-server communication

## Slide 51: Broadcast
Send a message to all recipients simultaneously
Used in DHCP, ARP (will be discussed later)

## Slide 52: Multicast
Transmit a single message to a group of recipients
One-to-many or many-to-many distribution
Examples:
  one person is talking on Skype with two other people
  sending e-mail message to a mailing list
  audio/video streaming

## Slide 53: Anycast
Traffic from a single sender is routed to the nearest node in a group of potential receivers
Advantages:
    better speed/performance
    enhanced reliability
Disadvantages:
    more difficult to implement and troubleshoot
    not supported by all protocols

## Slide 54
OSI and TCP/IP models

## Slide 55: OSI Model
OSI = Open Systems Interconnection
Why?
    Organizes the information
    Simplifies learning
    Standards for the vendors
    Easier troubleshooting
Protocol Data Unit (PDU) – different data format at each layer

## Slide 56: Layer 1 - Physical
The first and lowest layer
Transmitting raw bits
Wiring standards
Devices: hubs, repeaters, modems, cabling, connectors
Protocols: USB, Infrared, Bluetooth

## Slide 57: Layer 2 – Data Link
Switching functions
MAC addresses
Devices: switch, bridge, NIC
Protocols: VLAN, ARP, LLDP, CDP, STP

## Slide 58: Layer 3 – Network
Routing functions
IP addresses
Devices: router, L3 switch
Protocols: IP, ICMP (ping), RIP, OSPF, EIGRP, GRE, etc.

## Slide 59: Layer 4 – Transport
Provides “host-to-host communication”
Services:
  connection-oriented vs connection-less
  reliability (ACK, NACK)
  flow control
  multiplexing (port numbers)
Protocols: TCP, UDP

## Slide 60: TCP Three-Way Handshake
This is how TCP creates a connection over an IP network
a.k.a. “SYN, SYN-ACK, ACK” handshake

## Slide 61: TCP/UDP Twitter joke

## Slide 62: Layer 5 – Session
Opening, closing and managing a session
Services:
    Authentication
    Authorization
    Session restoration
Protocols: PPTP, L2TP, NetBIOS, RPC

## Slide 63: Layer 6 – Presentation
Sometimes called syntax layer
Acts as data translator for the network
Services:
    data conversion
    compression
    encryption/decryption

## Slide 64: Layer 7 – Application
End-user interaction with the network
Protocols: HTTP(s), FTP, SMTP, Telnet, SSH, RDP

## Slide 65: Mnemonics for the OSI Model
  Away
  Pizza
  Sausage
  Throw
  Not
  Do
  Please
  All
  People
  Seem
  To
  Need
  Data
  Processing

## Slide 66: Data Flow in the OSI Model

## Slide 67: Data Flow in the OSI Model (2)

## Slide 68: Encapsulation and decapsulation
Encapsulation
  Each layer adds its own header (and trailer)
  During the process, the packet goes down through the layers
Decapsulation
  Each layer removes the corresponding header (and trailer)
  During the process, the packet goes up through the layers

## Slide 69: The TCP/IP Model
Four-layer conceptual model similar to the OSI
Known as the Department of Defense (DoD) model
Why two models?
    They were both created independently

## Slide 70: OSI and TCP/IP Models Comparing

## Slide 71
Cisco Packet Tracer - Introduction
DEMO

## Slide 72: Summary
…
…
…
Basic networking concepts
IP and MAC addresses
Traffic types
OSI and TCP/IP models
Cisco Packet Tracer – Introduction

## Slide 74: SoftUni Diamond Partners

## Slide 75: Educational Partners

## Slide 76: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 76