## Slide 1: Course summary
Lecture 8
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Lecture 1: Introduction to networking
Lecture 2: IP addresses and host-to-host communication
Lecture 3: Network access, security and VLANS
Lecture 4: Layer 2 redundancy – STP
Lecture 5: IP services and basic routing
Lecture 6: Dynamic routing with OSPF
Lecture 7: Practice – Demonstrations with physical devices

## Slide 3
Lecture 1: Introduction to networking

## Slide 4: How did it start?
ARPANET - The Advanced Research Projects Agency NETwork
Established in 1969
It is the first packet switching network which will use TCP/IP
It was designed for scientific purposes and to share computer resources
ARPANET’s purpose was more academic than military

## Slide 5: Common Types of Computer Networks
Local Area Network (LAN)
Wide Area Network (WAN)
Wireless Local Area Network (WLAN)
Storage Area Network (SAN)
Home Area Network (HAN)

## Slide 6: Networks Protocols
Define a common format and set of rules for exchanging messages between network devices
Common protocols:
  HTTP
  FTP
  SMTP
  DNS
  DHCP
  RDP

## Slide 7: EIA/TIA Standards
EIA = Electronic Industries Alliance TIA = Telecommunications Industry Association
T568B is most frequently used

## Slide 8: OSI Model
OSI = Open Systems Interconnection
Why?
    Organizes the information
    Simplifies learning
    Standards for the vendors
    Easier troubleshooting
Protocol Data Unit (PDU) – different data format at each layer

## Slide 9: Data Flow in the OSI Model

## Slide 10: Data Flow in the OSI Model (2)

## Slide 11: OSI and TCP/IP Models Comparing

## Slide 12
Lecture 2: IP addresses and host-to-host communication

## Slide 13: Different numeral systems
Common Numeral Systems in computer networking:
Decimal
Binary
Hexadecimal

## Slide 14: IPv4 Address
Plays important role for device connectivity
It is a 32-bit address
There are 4 294 967 296 IP addresses (232)

## Slide 15: Private IP addresses
Used for addressing internal networks (offices, HQs etc.)
Not routable on the Internet
Can be reused in many networks
Range of private addresses for each class (classes are discussed later)

## Slide 16: NAT – Network address translation

## Slide 17: Network masks
Define the border between the network and the hosts part
Segment the network

## Slide 18: Reserved/Special IP Addresses
There are some special IP addresses. For example:
    127.0.0.1 /8
  Known as loopback address
  On most computer systems, “localhost” resolves to the IP address 127.0.0.1
    169.254.X.X /16
  When DHCP is not reachable
  Known as APIPA (Microsoft)

## Slide 19: Four addresses required
There are 4 addresses needed for Ethernet communication:
Source IP | Destination IP
Source MAC | Destination MAC

## Slide 20: ARP: Address Resolution Protocol
Used to find the MAC address of the destination
Uses Broadcast

## Slide 21: Direct communication (without router)
Source and destination MAC addresses are constant
Source and destination IP addresses are constant

## Slide 22: Host-to-Host Communication With Routers

## Slide 23: Host-to-Host Communication With Routers (2)
Source and destination MAC addresses are changed at every hop/router

## Slide 24: The MAC address table
It is a (dynamic) table that maps MAC addresses to ports
Used to find the proper interface when the switch forwards a packet

## Slide 25: Command Line Introduction
Different vendors use different names but the logic is similar
Typical CLI modes:
  Read-only (User)
  Read-write (Privilege)
  Configuration (Global config)
  Sub-configuration

## Slide 26: Command line
type “enable”
type “configure terminal”
Interface, VLAN, routing, etc.
to go back, type “exit”

## Slide 27: Basic Connectivity Checks
Ping (Layer 3)
Traceroute (Layer 3)
LLDP (Layer 2)
CDP (Layer 2)

## Slide 28
Lecture 3: Network access, security and VLANS

## Slide 29: Saving the configuration
The configuration file must be saved to survive reboot
To save the running configuration file (stored in RAM) to the startup configuration file (stored in NVRAM), use either:
    copy run start
    write memory
running config
startup config
configuration
changes

## Slide 30: Loading the configuration
The saved configuration file (startup config file) will go in the RAM (the running config file) when:
  the device is restarted
  a copy start run command is executed
running config
startup config

## Slide 31: Out-of-band vs in-band management
Out-of-band:
    Management traffic uses separate path from the user traffic
    Typical protocol: Console
In-band management
    Management traffic travels the same path as user traffic
    Typical protocols: Telnet, SSH, SNMP, Web

## Slide 32: Secure access - best practices
Physically secure the devices
Use SSH instead of Telnet
Use SNMPv3 instead of v1 or v2
Use HTTPS instead of HTTP
Out-of-band management (console) is considered more secure than in-band management
Create strong passwords for each privilege level and method of access (console, VTY)

## Slide 33: Access (untagged) ports
Used to connect to end-user devices
Can be associated with only one VLAN
Uses the “normal” ethernet frame where there is no VLAN information - no VLAN tag

## Slide 34: Trunk (tagged) ports
Used to connect between switches
Can carry information from/to multiple VLANs
Uses the 802.1Q tagged frame

## Slide 35: Tagging between switches
Untagged
VLAN 2
Untagged

## Slide 36: Trunk port details
Uses IEEE 802.1Q tag to identify each frame
A trunk carries multiple tagged VLANs and (maximum) one untagged VLAN
The untagged VLAN on a trunk is called:
    Native VLAN (Cisco)
    PVID (HPE Comware)
    Untagged VLAN (HPE Provision)

## Slide 37
Lecture 4: Layer 2 redundancy - Spanning Tree Protocol

## Slide 38: What is the Spanning Tree Protocol?
It addresses a problem which switches can not handle alone: the broadcast storms
Without STP, a L2 loop will:
    Overload the links
    Affect the end devices
    Cause MAC table instability
    …never stop

## Slide 39: What is the Spanning Tree Protocol? (2)
All STP enabled switches “talk” to each other
The management information that they exchange is in the form of BPDUs (Bridge Protocol Data Units)
The goal is to logically block one or more ports to prevent from loops

## Slide 40: The STP algorithm
Elect the Root switch (Root bridge)
    This is the switch with the lowest BID (Bridge ID)
    BID = Switch Priority and MAC
Select the root ports
    They have the best cost (lowest) to the Root
    Selected per switch
Select the designated ports
    They have the best cost (lowest) to the Root
    Selected per segment (connection)
All other ports go to blocking state

## Slide 41: STP tie-breakers
If there is a tie situation - the same path cost via different paths, use the following tie-breakers:
    When selecting Root port or Designated port, chose the neighboring switch which has the lowest Bridge ID
    If the Bridge ID is the same, select the lowest Port ID (PID)
    Port ID = Port priority and port number

## Slide 42: Link costs (path cost)
Higher port speed -> lower cost
The values can be changed by administrator

## Slide 43: STP Priority
A number between 0 and 61440
Must be configured in increments of 4096
Default is 32768 (+ the VLAN ID)
The switch with the lowest priority will become the Root
If equal values -> lowest MAC address wins (BID = Priority and MAC)

## Slide 44: Spanning Tree Protocol – Main Flavors
STP - Spanning Tree Protocol, IEEE 802.1D
RSTP - Rapid STP, IEEE 802.1W
MSTP - Multiple STP, IEEE 802.1S (802.1Q-2005)
PVST+ - Per-VLAN STP, Cisco proprietary

## Slide 45: PVST+
Per-VLAN Spanning Tree is Cisco protocol
Why? It has a similar idea as MSTP -
Creates a spanning tree topology separately
PortFast in PVST+ is similar to Edge port in STP/RSTP
to distribute the load
for each VLAN

## Slide 46: PVST+ (3)
Switch 2
Switch 3
Vlan 1
Vlan 2
Priority: 0
Priority: 4096
Priority: 32768
Priority: 32768
Priority: 0
Priority: 4096
R
R
Switch 1
Vlan 1
Vlan 2
Vlan 1
Vlan 2
port 1
port 2
port 1
port 2
port 1
port 2

## Slide 47: The good and the bad about PVST+
PVST+ advantages:
  triggers STP calculation only if there is a potential loop in a particular VLAN
  detailed “look” of the network – does not block ports when there is no loop on the trunks for a given VLAN
  PVST+ disadvantages
  generates a lot of overhead in the network
  proprietary protocol

## Slide 48
Lecture 5: IP services and basic routing

## Slide 49: What is DHCP?
DHCP: Dynamic Host Configuration Protocol
Provides automatic distribution of IP addresses and other networking parameters such as:
    Subnet mask
    Default gateway
    DNS servers
    More…
Industry standard

## Slide 50: DHCP Components
Server
    DHCP scope - range of addresses (pool), lease time, reservations, etc.
    Uses port UDP 67
Client
    Must be configured to use DHCP
    Uses port UDP 68
(Relay agent)
    Used to serve multiple (V)LANs with a single DHCP server

## Slide 51: DNS Introduction
DNS: Domain Name System
DNS Usage:
    To translate names to IP addresses
    To translate IP addresses to names
    To find a particular service in the network
*DNS will be discussed in more details in the advanced course

## Slide 52: DNS “A” Records
One of the most commonly used records in DNS
Matches a hostname (or FQDN) to an IP address
Examples:
  pc1 -> 192.168.1.1
  pc2 -> 192.168.1.2
  server -> 192.168.1.100
  www.abv.bg -> 194.153.145.104
*FQDN = Fully Qualified Domain Name

## Slide 53: Switching vs Routing
Switches:
    Use Layer 2 information (MAC addresses)
    Forwarding decisions based on the MAC address tables
    Not scalable for big networks
    Routers:
        Use Layer 3 information (IP addresses)
        Forwarding decisions based on the routing tables
        Scalable for large networks

## Slide 54: The Routing Table
My routing table:
192.168.5.0/24 via 10.1.1.1
172.16.0.0/16 via 10.15.15.1
87.15.23.0/24 via 10.23.23.1
10.1.1.0/24 is local
10.15.15.0/24 is local
10.23.23.0/24 is local
10.1.1.100
10.15.15.100
10.23.23.100

## Slide 55: Default Gateway

## Slide 56: The Rule of the Longest Match
192.168.0.0/16 via 10.1.1.1
192.168.5.0/24 via 10.15.15.1
0.0.0.0/0 via 10.23.23.1
How do I reach 192.168.5.3?
How do I reach 192.168.18.7?
How do I reach 85.12.3.42?
Answer: via 10.15.15.1
Answer: via 10.1.1.1
Answer: via 10.23.23.1

## Slide 57: Direct routing

## Slide 58: Inter-VLAN Routing Using the Same Switch

## Slide 59: Inter-VLAN Routing Using External Switch
Trunk ports
(This is L3 switch)
(This is L2 switch)

## Slide 60: Inter-VLAN Routing Using External Router (2)
Trunk port

## Slide 61: Static Routes
10.1.1.0/24 is local
192.168.1.0/24 is local
192.168.2.0/24 via 192.168.1.2
10.2.2.0/24 via 192.168.1.2
192.168.1.0/24 is local
192.168.2.0/24 is local
10.1.1.0/24 via 192.168.1.1
10.2.2.0/24 via 192.168.2.3
192.168.2.0/24 is local
10.2.2.0/24 is local
10.1.1.0/24 via 192.168.2.2
192.168.1.0/24 via 192.168.2.2

## Slide 62
Lecture 6: Dynamic routing with OSPF

## Slide 63: Distance-vector vs link-state protocols
Distance-vector protocols
Link-state protocols

## Slide 64: RIP Metric: hop count
I will use Router1!
I know how to reach Destination!
I know how to reach Destination!
Note: all routers talk RIP

## Slide 65: OSPF Metric: cost
I will use Router3!
slow links
fast links
I know how to reach Destination!
I know how to reach Destination!
Note: all routers talk OSPF

## Slide 66: Multiple protocols in the same network
?
slow links
fast links
Note: all routers talk RIP and OSPF
RIP: I am better to reach Destination!
OSPF: I am better to reach Destination!

## Slide 67: Administrative distance

## Slide 68: Wildcard masks
In the subnet masks, 1 means “do care” and 0 means “don’t care”
Examples:
    192.168.1.0 255.255.255.0 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 255.255.255.255 -> exact IP address
    In the wildcard masks, 0 means “do care” and 1 means “don’t care”
    Examples:
    192.168.1.0 0.0.0.255 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 0.0.0.0 -> exact IP address

## Slide 69: OSPF terms: router ID
I have many names (interfaces), but just call me 2.2.2.2
Hi, 2.2.2.2!
Hi, 2.2.2.2!

## Slide 70: OSPF terms
Autonomous system
ASBR
ABR
ABR
Area 0 = the backbone area

## Slide 71: Single area OSPF configuration
Minimum configuration:
  router ospf process_id
  router-id number (optional)
  network A.B.C.D wildcard_mask area number
Example:
  router ospf 1
  router-id 1.1.1.1 (optional)
  network 192.168.1.0 0.0.0.255 area 0
  network 10.0.0.0 0.0.0.255 area 0

## Slide 72: OSPF passive interface
The “network” command advertises the network AND sends hello messages out of the interface
What if there is non-OSPF device on the other end of the link?
    The Hello packets will be useless
    Represents security issues
    One solution: use passive interfaces

## Slide 73: OSPF passive interface (2)
R1:
network 10.0.0.0 0.0.0.255
R2:
network 10.0.0.0 0.0.0.255
network 20.0.0.0 0.0.0.255
10.0.0.1
10.0.0.2
20.0.0.1
Hello!
I have network 10!
Hello!
Hello!
…and 20!
I have network 10!
I have network 10 and 20!
G0/1
passive-interface G0/1

## Slide 74
Lecture 7: Demonstrations with physical devices

## Slide 75
Corporate WEB and DNS Server
fa0/1
fa0/2
ge1/0/1
ge1/0/2
ge1/0/3
VLAN 5 (guest): 10.5.5.0/24
VLAN 10 (corporate): 10.10.10.0/24
Internet
ether 1
ether 5
SSID:
NetFund-Corporate
SSID:
NetFund-Guest
Ruckus AP
ZoneFlex 7363
Cisco 3560 PoE
3COM
MikroTik
RB951Ui-2HnD
Demo - scenario 1

## Slide 76: Topology details – scenario 1
DHCP server for both VLANs is the Cisco device
MikroTik is routing the VLANs and making NAT to “outside”
Device, interface | IP address
Cisco, VLAN 5 | 10.5.5.3
Cisco, VLAN 10 | 10.10.10.3
HP, VLAN 5 | (10.5.5.2)
HP, VLAN 10 | (10.10.10.2)
Corporate server (Web and DNS) | 10.10.10.101
MikroTik, VLAN 5 | 10.5.5.1
MikroTik, VLAN 10 | 10.10.10.1

## Slide 77
Corporate WEB and DNS Server
DHCP
fa0/1
fa0/2
VLAN 5 (guest): 10.5.5.0/24
VLAN 10 (corporate): 10.10.10.0/24
Internet
ether 1
ether 5
SSID:
NetFund-Corporate
SSID:
NetFund-Guest
Ruckus AP
ZoneFlex 7363
Cisco 3560 PoE
MikroTik
RB951Ui-2HnD
Demo - scenario 2
fa0/3
10.23.23.0/24
10.13.13.0/24

## Slide 78: Topology details – scenario 2
DHCP server for both VLANs is the (Windows) Server
Cisco is routing the VLANs, MikroTik is making NAT to “outside”
Device, interface | IP address
Cisco, VLAN 5 | 10.5.5.3
Cisco, VLAN 10 | 10.10.10.3
Cisco, fa0/3 | 10.13.13.3
Cisco, fa0/2 | 10.23.23.3
Corporate server (Web and DNS) | 10.13.13.101
MikroTik, ether 5 | 10.23.23.1

## Slide 79: Summary
…
…
…
1. Lecture 1: Introduction to networking
2. Lecture 2: IP addresses and host-to-host communication
3. Lecture 3: Network access, security and VLANS
4. Lecture 4: Layer 2 redundancy – STP
5. Lecture 5: IP services and basic routing
6. Lecture 6: Dynamic routing with OSPF
7. Lecture 7: Practice – Demonstrations with physical devices

## Slide 81: SoftUni Diamond Partners

## Slide 82: Educational Partners

## Slide 83: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 83